## Slide 1: Applying Off-the-Shelf Technologies in eVLBI
  Ari Mujunen, Ari.Mujunen@hut.fi
  Metsähovi Radio Observatory
  Helsinki University of Technology

## Slide 2: Outline
Overview of available off-the-shelf technologies
Evaluation test results
Current technology limitations
Impact of technology limitations on system design and system scalability
Near-future off-the-shelf trends
A strategy for an uninterrupted 1Gbps eVLBI system

## Slide 3: Overview of Available Off-the-Shelf Technologies
COTS: means mainstream technology, used by millions of people
Tremendous R&D investments by industry in general-purpose COTS disk, computer, tape, and networking technologies
Thus industry does R&D for us faster than we can do on our own
Only if we can directly use standard technologies without locking to them

## Slide 4: COTS Disks and Computers
Both are evolving at exponential “Moore rate” with no signs of slowdown
Sizes have
tripled since
the start of
disk recorder
projects!

## Slide 5: COTS Tapes and Networking
Faster high-capacity tapes “in the works”
  Sony S-AIT-1(,2,3,4), Quantum SDLT, HP/IBM/Seagate LTO2
    500GB, 320GB, 200GB / 240Mbps, 128Mbps, 240Mbps...
  Expensive drives (~$10k) and tapes; still slow; not at all a mainstream technology
Networking migrates 100M->1G->10Gbps
  ATM and others losing to Ethernet
  1Gbps Ethernet becoming mainstream

## Slide 6: Evaluation Test Results
Dell PE1600SC with ServerWorks GC-SL
  On paper, multi-Gbps
  In practice, 400-500Mbps with ~70% CPU load!
    Two Promise IDE PCI ctrls
    Single rd 600, wr 700Mbps
    rd+wr: rd 400 + wr 550Mbps
    VSIB rd+wr: the same
    Sum of I/O always <1Gbps..
32
1.6GB/s
3.2GB/s
3.2GB/s

## Slide 7: Evaluation Test Results
MSI K7N2G-ILSR with nVidia nForce2
  On paper only PCI32/33, <1Gbps
  In practice 0.7Gbps from and 0.4Gbps to PCI board <-> on-board IDE with only ~45% CPU load
Parallel ATA disks not suitable for >45cm cabling; limited COTS solutions to disk swaps
  Longer cables force reducing speed from UDMA133/100 to UDMA66 or even UDMA33
    UDMA33 allows only 120Mbps/disk (half of native perf.) -> 9 disks needed for 1Gbps

## Slide 8: Current Technology Limitations
Low-cost computers have just gained the capability to reach 0.5Gbps in all directions
  PCI(net/VSIB)<->memory<->disk
The leap to >1Gbps will probably happen only after 1Gbps networking has replaced 100Mbps everywhere (2005?)

## Slide 9: Impact of Limitations on System Design
All subsystems achieve 0.5Gbps but 1Gbps is difficult/flaky
  Input/Output (PCI)
  Memory, CPU
  Disks
  1Gbps Ethernet
So let's make a scalable 0.5Gbps box!
  Affordable enough, can buy as many as needed
  Standard enough, can replace when needed

## Slide 10: MVR Recorder with VSIB Board
0.5Gbit/s for
1200 euros!
VSI-H compatible
Chainable for:
  More speed
  More on-line storage

## Slide 11: Near-Future Off-the-Shelf Trends
Large Serial ATA (SATA) disks replace PATA
  $1/GB, drops quickly (600GB for $300 in 2004?)
1Gbps Ethernet everywhere
Backups migrate from tape -> disks
  SATA native hot/warm swap connectors
HyperTransport, PCI Express, ...
Intel 875P

## Slide 12: Motherboard Trends
Multiple high-speed channels to memory
  Intel E7501 2x Xeon, 3x HI2.0, 1x HI1.5
  Intel E7505 (1x HI 2.0)
AMD Opteron with 3x 6.4GB/s HyperTransport
  nVidia nForce 3 Pro chipset
  AMD-8000 chipset

## Slide 13: A Strategy for an Uninterrupted 1Gbps eVLBI System
MMM
4x MVR (or MVR chains)
Mk4 Fmt
1Gbps Switch
Set #1
Set #2
VSIC
VSIC
VSIB
VSIB
VSIB
VSIB
“CoolSwap”

## Slide 14: An Example
3.5h of 2 Gbps onto 16 200GB disks
Or continuously 1Gbps onto 8 disks, swapping the other 8 every 3.5h
Only 9477 euros
  (plus disks)
  Incl. 19in rack & 4x Gbps Ethernet /w 8-port switch
MMM
4x MVR

## Slide 15: Metsähovi VSI Data System Evolution